## Slide 1: Distributed Generation Monitoring Tool
Duke Energy Carolinas – Grid Solutions – Joe Lavalliere – 2015

## Slide 2: Outline
The Need for a Distributed Generation (DG) Monitoring Tool
Getting Started – The Available Displays
  “DEC Visuals”
    DEC Geographic View
    DEC Dashboard
    Distributed Energy Resources (DER) Tabular Display
  “Individual Displays”
    PV site Characteristics and Real-Time measurements
  “Landfill Gas & Hydro Facilities”
Aggregate DER PI Tags to be pushed to EMS

## Slide 3: The Need for a Distributed Generation Monitoring Tool (1 of 3)
Chart: DEC’s Non-Utility Generation (NUG) Status as of June 18th, 2015
| Connected | Active PI Tags | Under Construction | Pending
Biomass | 4.6 | 2.3 | 5.2 | 0
Hydro | 29.5 | 19.2 | 0 | 4
Landfill Gas | 40.76 | 39.89 | 0 | 1.6
Solar | 155 | 134.3 | 144.98 | 344.9
Solar capacity will almost double once Solar Facilities finish construction!

## Slide 4: The Need for a Distributed Generation Monitoring Tool (2 of 3)
Chart: DEC’s Annual Connected Solar
| 2010 | 2011 | 2012 | 2013 | 2014
Connected Solar | 5.051 | 16.5 | 17.5 | 28.5 | 67.23
Almost 70MW was added in just 2014 alone.
2015 data was not included because many sites are still under construction. This is projected to be 100+ MW.
This data only includes utility scale sites with electronic reclosers.

## Slide 5: The Need for a Distributed Generation Monitoring Tool (3 of 3)
Currently, there is a total of ~200MW of Non-Utility Generation (NUG) with 150MW under construction connected at a distribution level service. This will be 350MW of NUG.
DCC Operators and Engineers do not have a convenient way to monitor DERs on network using DMS/DOMS.
This tool will make people aware of the voltage swings and that connected solar sites are causing reverse power flow on the substation.
Chart: DEC'S DER Generation Profile

## Slide 6: Getting Started – The Available Displays
When the file is first opened, three tabs will be are available for you to select.
“DEC Visuals” Provides high-level views of DER operation.
“Individual Displays” Provides a detailed display of each Solar Facility.
“Landfill Gas & Hydro” Provides multiple sites per display of only single phase recloser RT data and three phase power generation.
“DEC_GEOGRAPHIC” is the main PI Display that was designed to fit on a DCC wall-mounted TV. More detail on next slide.

## Slide 7: “DEC Visuals” - DEC Geographic View (1 of 2)
Site Symbols:
  Hover-over: Displays PV Site Name with PPA (MW) amount.
  Single Click: Navigates to the PV Site’s individual display.
Satellite Image Update:
  Observation: Time of Update.
  Every 2 minutes an update occurs that will refresh the satellite image and location of site symbols.
Distributed Generation Profile:
    Observation: R.T. & previous 8hrs of Total DER Generation along with Solar (PV) Generation.
1
3
2

## Slide 8: “DEC Visuals” - DEC Geographic View (2 of 2)
Site Symbol LEGEND:
  Multi-State Conditions: Site symbol color is dependent on its R.T. power output. Base of percentage is the PP or Nameplate MW.
  Flashing Condition: Occurs when there is reverse power flow observed at the upstream feeder circuit breaker.
VIEW CONTROLS:
  Button Action: A single click of a square will hide/show DER sites.
TOTAL DER GEN:
    Visual Aid: Displays relation of maximum telemetered MW and R.T. MW measurement.
6
5
4

## Slide 9: “DEC Visuals” - DEC Dashboard (1 of 2)
“DEC Visuals” - DEC Dashboard Display. Double click title to open.

## Slide 10: “DEC Visuals” - DEC Dashboard (2 of 2)
PV Site Action Button:
  Single Click: This will navigate you to the Individual Site PI display.
Three Phase Power Output:
    Observation: Displays the three phase power output of the solar site, all on a 5,000kW scale.
    Provides the user a quick way to inspect the operation of all PV sites.
1
2

## Slide 11: “DEC Visuals” – DER Tabular Display (1 of 2)
“DEC Visuals” - DEC Tabular Display. Double click title to open.

## Slide 12: “DEC Visuals” – DER Tabular Display (2 of 2)
RT Value:
  Observation: Provides the real-time MW generation of each type of DER. Updated every minute.
TELE Capacity:
    Observation: Provides a static reference to the available capacity of operational PI tags.
Regional Solar:
    Observation: Provides the real-time MW Solar generation broken down into DEC regions.
2
3
1

## Slide 13: “Individual Displays” – PV Site Characteristics & RT Operation (1 of 3)
“Landfill Gas & Hydro Facilities” – Site Characteristics & R.T. Operation. Double click title to open.
Over 12+ displays created.
“Individual Displays” – PV Site Characteristics & R.T. Operation. Double click title to open.
Over 50+ displays created.

## Slide 14: “Individual Displays” – PV Site Characteristics & RT Operation (2 of 3)
2
3
1
Site Description:
  Information: Provides the user with feeder name, location, technical specifications, and Site Contact.
Arial Site View:
  Google Maps image along with exact Latitude, Longitude of site.
Recloser & Breaker – Single Phase Real Power (kW):
    Observation: Displays raw data of single phase kw measurements of the site recloser and its feeder’s circuit breaker at the substation.

## Slide 15: “Individual Displays” – PV Site Characteristics & RT Operation (3 of 3)
Three Phase Real Power (kW):
  Summation of single-phase measurements from reclosers:
(Feeder name) %DER:
  Provides the ratio of generation to feeder load. Greater than 100% equates to reverse power flow.
Voltage Profile of DER & Feeder CB:
    Observation: Displays raw data of single phase voltages of the site recloser and its feeder’s circuit breaker at the substation. Converted to 120V base.
5
4
6

## Slide 16: Aggregate DER PI Tags to be pushed to EMS
The follow tags are available in PI-Server CLTECRDPIP1 for an easy means to pull historical data and push real-time values to EMS servers.
Each TOTAL tag has (2) other tags associated with it, a .GROSS & .COUNT

## Slide 18: Salesforce Data Overview
Chart: DEP DER Summary
| Connected | Active PI Tags | Under Construction | Pending
Biomass | 0.27 | 0 | 0 | 3.02
Hydro | 17.17 | 0 | 0 | 0
Landfill Gas | 29 | 0 | 9.6 | 9.6
Solar | 480 | 0 | 197 | 1389